## Slide 1
01
AGERE
A Safe Integration Architecture for AI-Driven Autonomous Flight
PROJECT APPROVAL PRESENTATION | JULY 2026

## Slide 2
02
THE AUTONOMY DILEMMA
THE SAFETY GAP
Autonomous systems face a trade-off: advanced AI reasoning can enable better decisions but also introduces nondeterministic behavior that is risky in safety-critical systems. Human-in-the-loop rules reduce risk but limit autonomy.
THE RISK OF HALLUCINATION
Direct AI control risks unpredictable failures; large models are powerful but not yet suited for hard real-time motor control. A principled middle ground keeps deterministic safety while using AI strategically.
"Not to replace the pilot, but to provide a principled middle ground for safe autonomous judgment."

## Slide 3
03
THE HIERARCHICAL ARCHITECTURE
01
STRATEGIC LAYER
Runs on a companion computer (Jetson). Handles high-level reasoning, LLMs, and vision models. Powerful but non-deterministic.
02
TACTICAL LAYER
The "Safety Enforcer." Acts as a translator and gatekeeper between AI suggestions and flight execution.
03
EXECUTION LAYER
PX4 on Pixhawk. Handles real-time control and failsafes. Deterministic, safety-certifiable, and the ultimate authority.
THE BASE GUARANTEE
The architecture ensures a strict chain of command. All communication flows through a uXRCE-DDS bridge over ROS 2.
If the Strategic Layer (AI) crashes, the Execution Layer (PX4) continues flying safely, maintaining stability and executing pre-defined failsafe procedures.
"Think of it as a military command structure: the AI advises, but the flight controller executes only what is safe."

## Slide 4
04
VERSION 2.0 ENHANCEMENTS
GROUND-LINK-LOSS FRAMEWORK
Defines phase-aware behavior when comms are lost: in transit the drone continues and retries connection; in search it loiters and records imagery to avoid acting on unconfirmed detections.
THE WORK INDEX MODEL
Continuous energy-margin assessment that decides mission completion or triggers abort/emergency landing when thresholds indicate unsafe return.
Logic-First Design: rigorous state and decision rules, leaving hardware constants to field calibration.

## Slide 5
05
SAFETY PHILOSOPHY
RIGID ISOLATION
The architecture enforces a strict boundary between non-deterministic AI and hard real-time control. AI suggests mission parameters but is physically and logically barred from bypassing PX4's core safety layers, including geofences and motor speed limits.
HEARTBEAT MONITORING
PX4 continuously monitors the health of the companion computer. If a heartbeat timeout is detected—indicating an AI freeze or hardware crash—the system immediately transitions to a deterministic failsafe state.
Failsafe Sequence:
1. Detect Missing Heartbeat; 2. Transition to Position Hold; 3. Execute Autonomous Landing

## Slide 6
06
PROJECT SCOPE & DELIVERABLES
CORE DELIVERABLES
01
ARCHITECTURAL SPECIFICATION
Full Version 2.0 documentation including formal decision tables and energy-margin equations.
02
SIMULATION VALIDATION
Gazebo SITL testing with injected link dropouts and battery drain to verify logic behavior.
03
MVP INTEGRATION
A functional ROS 2 node demonstrating trajectory streaming and the uXRCE-DDS bridge.
PHASE BOUNDARIES
CURRENT FOCUS
This approval cycle is strictly for Architecture and Simulation Validation. The goal is to prove the logic before hardware implementation.
OUT OF SCOPE
Field-tuned constants, dual-battery hardware design, and landing-site computer vision are deferred to future work.

## Slide 7
07
CONCLUSION & PROPOSAL
PRACTICAL VALUE
The Agere architecture provides a principled middle ground for autonomous operations where failure is not an option. By isolating AI reasoning from deterministic control, we enable drones to maintain mission utility in radio-silent environments without compromising safety.
"I am not trying to replace the pilot. I am giving the drone enough judgment to stay safe when the pilot goes quiet."
FORMAL REQUEST
01
Approval of the system design as the formal project scope.
02
Access to lab simulation environments for SITL/Gazebo validation.
03
Milestone review in 4–6 weeks to evaluate simulation results.